NEW!!! DP-6880 Heavy Duty Airless Paint Sprayer

| Model number | DP-6880 |
| --- | --- |
| Motor power | 4HP 3000W |
| Voltage | 380V or 220V |
| Max. flow rate | 8L/min |
| Max. pressure | 25Mpa / 250bar / 3300psi |
| Max. tip size | 0.041” |
| Length of standard hose | 10mm*10m /1 roll, 8mm*10m / 1 roll, 8mm*2m / 1roll |
| Max. length of hose | 90m |
| Dimension | 56*67*79cm |

# Text boxes

Pressure Gage

Pump Manifold

Pressure Gage

Electric control box

adjustable frame

Oil cup

Prime/Spray Valve

Outlet fitting

Pressure regulator

Durable fluid pump

Power plug

Big s.s. Suction filter

Wheel

Ningbo Dino-Power Machinery Co.,Ltd.

Website: www.dpairless.com

Features

*Equipped with 3 phase asynchronous motor, low round speed but very strong power.

*Long-life chromate treatment Piston Rod, Sleeve, oversized Packings(Total 16pcs.).

The Piston rod&V-packing are 4MM bigger than the DP-6850 which offer much more delivery volume.

* Durable and accurate electric control box.

*Build-in tool box for easy store up of the frequently-used tools and spare parts like tip, packing, filter etc.

Applications:

Spraying texture, white cement, putty, plastering, inorganic zinc coating , epoxy zinc-rich primer,etc

Accessories